Install raspbian.

Find address of router using:
route -n
where the destination is 0.0.0.0 the gateway is the location of the router

Find mask and current id using ifconfig (if on wifi use wlan0 on ethernet use eth0):

edit /etc/network/interfaces:
auto lo

iface lo inet loopback
iface eth0 inet static
address [desired address(must be on same subnet as router)]
netmask 255.255.255.0
gateway [address of router]

allow-hotplug wlan0
iface wlan0 inet manual
wpa-roam /etc/wpa_supplicant/wpa_supplicant.conf
iface default inet dhcp
iface khyber inet static
address [desired address(must be on same subnet as router)]
netmask 255.255.255.0
gateway [address of router]

edit /etc/wpa_supplicant/wpa_supplicant.conf:
network={
ssid=[your ssid]
psk=[your wifi password]
id_str=[a name for this connection]

ssh into the pi using:
ssh pi@[pi address]

install apache:
sudo apt-get install apache2 libapache2-mod-wsgi php5-cgi php5-cli libapache2-mod-php5

test gpio with:
import RPi.GPIO as gpio
import time

gpio.setmode(gpio.BOARD)
gpio.setup(12, gpio.OUT)
gpio.output(12, True)
gpio.setup(10, gpio.OUT)
gpio.output(10, False)
time.sleep(1)
gpio.output(12, False)

this must be run with sudo python. Attach some sort of test circuit to rxd and pin 18 Numbers

RPi.GPIO	Raspberry Pi Name	BCM2835
P1_01	1	3V3
P1_02	2	5V0
P1_03	3	SDA0	GPIO0
P1_04	4	DNC
P1_05	5	SCL0	GPIO1
P1_06	6	GND
P1_07	7	GPIO7	GPIO4
P1_08	8	TXD	GPIO14
P1_09	9	DNC
P1_10	10	RXD	GPIO15
P1_11	11	GPIO0	GPIO17
P1_12	12	GPIO1	GPIO18
P1_13	13	GPIO2	GPIO21
P1_14	14	DNC
P1_15	15	GPIO3	GPIO22
P1_16	16	GPIO4	GPIO23
P1_17	17	DNC
P1_18	18	GPIO5	GPIO24
P1_19	19	SPI_MOSI	GPIO10
P1_20	20	DNC
P1_21	21	SPI_MISO	GPIO9
P1_22	22	GPIO6	GPIO25
P1_23	23	SPI_SCLK	GPIO11
P1_24	24	SPI_CE0_N	GPIO8
P1_25	25	DNC
P1_26	26	SPI_CE1_N	GPIO7